## Slide 1: Decision Support System for Matrix Diffusion Modeling
Charles Newell and Shahla Farhat
GSI Environmental Inc.

## Slide 2: Acknowledgements
Dr. Tom Sale, Colorado State
Dr. Beth Parker, U. of Guelph
SERDP/ESTCP
Schlumberger, Geosyntec
USEPA TIO

## Slide 3
Introduction
Matrix Diffusion Background
Options for Modeling Matrix Diffusion
Introduction to MDT – Square Root Model
Dandy-Sale Model in the MDT
Case Study 1
Case Study 2
Wrap-up and Open Discussion
Road Map

## Slide 4: Mini Road Map
Matrix Diffusion Background
Lines of Evidence
New Conceptual Model
Collecting Field Samples

## Slide 5: What is Diffusion?
Diffusion describes the spread of particles through random motion from regions of higher concentration to regions of lower concentration.
Key people: Fourier (1822), Fick (1855), Einstein (1905), Smoluchowski (1906)
Coffee Cup: Convection + diffusion
Laminar Groundwater: Molecular diffusion - movement of molecules only
J = D
dC
dx
J = Diffusive flux flowing though a particular cross section (mg/ meter2 / sec)
D = Diffusion coefficient (meter2 / sec)
= Concentration gradient
(mg / liter / meter)
dC
dx
4

## Slide 6
Goodall and Quigley (1977): Core analysis.
Foster (1975): Chalk system in England.
Where is the tritium going?
Matrix diffusion (30 cm penetration in clay) vs. advection in clay (4 cm). Matrix Diffusion “overwhelms” advection..
5
Incomplete History of Matrix Diffusion in Groundwater

## Slide 7
Sudicky, Gillham, and Frind (WRR: 1985):
“…these effects are the result of a transient redistribution of the tracer across the strata by transverse molecular diffusion …”
6
Incomplete History of Matrix Diffusion in Groundwater

## Slide 8
“As plumes spread through aquifers, the dissolved contaminants move quickly through more permeable zones while they slowly invade the less permeable ones by flow or diffusion.”
“Over the years and decades, this invasion can cause the plume to occupy large volumes of low permeability material. To obtain clean water from wells, it is generally necessary for the lower permeability parts of the aquifer system to be cleaned as well as the high permeability zones.
Mackay and Cherry (ES&T: 1989)
7
Incomplete History of Matrix Diffusion in Groundwater

## Slide 9
Parker, Gillham, Cherry (G. W.: 1994):
Matrix diffusion can soak up DNAPL in fractures – sometimes really quickly (days to weeks).
8
Incomplete History of Matrix Diffusion in Groundwater

## Slide 10
Chapman and Parker (WRR: 2005).
“Vertical back diffusion from the aquitard combined with horizontal advection and vertical transverse dispersion account for the TCE distribution in the aquifer and that the aquifer TCE will remain much above the MCL for centuries.”
9
Modified from figure in Chapman and Parker, 2005.
Incomplete History of Matrix Diffusion in Groundwater

## Slide 11: Frequently Asked Questions (Sale et al, 2008)
Provides quick access to key concepts and references for those who need to know more
Matrix-diffusion centric
Tom Sale, Chuck Newell, Hans Stroo, Rob Hinchee, and Paul Johnson
August 2008
Tom Sale, Charles Newell, Hans Stroo, Robert Hinchee, and Paul Johnson
Frequently Asked Questions Regarding Management of Chlorinated Solvents in Soils and Groundwater
10

## Slide 12
Transport at time t with dispersion
• Advection
• Dispersion
Old Plume Paradigm?
Advection Dispersion Model
• Adsorption
• Biodegradation
11

## Slide 13: New Plume Paradigm Heterogeneity Rules, Even in “Sandy Aquifers”
Image from Fred Payne /ARCADIS
Matrix Diffusion Paradigm:
Remediation Hydraulics (CRC Press)
Fred Payne, Joseph Quinnan, Scott Potter
12

## Slide 14: New Plume Paradigm Matrix Diffusion
After NRC 2005
13

## Slide 15: Where is Matrix Diffusion Important?
After NRC 2005
YES
YES
YES
?
?
14

## Slide 16
Matrix Diffusion Background
Lines of Evidence
New Conceptual Model
Collecting Field Samples
Mini Road Map

## Slide 17: Two layer sand tank study Colorado School of Mines (Tissa Illangasekare and Bart Wilkins)
56cm
45 cm
#30 Sand
#140 sand
1,1,2
-
TCA DNAPL
Pool 2.5 x 10 cm
18 cm
Groundwater
Flow 1.5 ft/day
56cm
45 cm
#30 Sand
#140 sand
1,1,2
-
TCA DNAPL
Pool 2.5 x 10 cm
18 cm
Groundwater
Flow 1.5 ft/day
AFCEE Source Zone Initiative (2007)
16
Notes: 16

## Slide 18
NO DNAPL
YES DNAPL
Remaining DNAPL by X-ray adsorption
Cumulative Mass Discharged
AFCEE Source Zone Initiative (2007)
Distribution of TCA Mass Recovered vs. Time
Mass in low permeability layer
Distribution of TCA Mass Recovered vs. Time
17
Notes: 17

## Slide 19
18
Matrix Diffusion Movie Doner and Sale, Colorado State University
Notes: 18

## Slide 20
Loading Phase
To Download: www.gsi-net.com
Matrix Diffusion Movie Doner and Sale, Colorado State University
19

## Slide 21: Matrix Diffusion Movie Doner and Sale, Colorado State University
Flushing Phase
To Download: www.gsi-net.com
20

## Slide 22
Matrix diffusion governed by concentrations gradients that occur at scales of centimeters to millimeters.
107 cm
84 cm
A
B
C
D
Day 28
Key Point – Matrix Diffusion is a Small Scale Phenomena
21

## Slide 23
Connecticut Site
Source
Zone
Groundwater
Flow
N
Transect 1
500 ft
Chapman and Parker WRR 2005
Image Courtesy of B. Parker
22
Notes: 22
22
Aerial photograph – source area east of facility, monitoring transect along west side of facility 900 ft from source along entire width of facility (~1400 ft).

## Slide 24: High-Resolution Data from Core
Aquifer
Aquitard
Aquifer
Aquitard
Chapman and Parker, 2005
23
Notes: 23
23

## Slide 25
500 ft
Modified from figure provided by B. Parker. Source of Data: Chapman and Parker, 2005.
3000 kg TCE present in low-perm zone!
Source
Zone
Groundwater Flow
Transect 1
N
24
Notes: RITS Spring 2008: Dilute Groundwater Plume Management
24
24
Aerial photograph – source area east of facility, monitoring transect along west side of facility 900 ft from source along entire width of facility (~1400 ft).

## Slide 26: Concentration vs. Time from Monitoring Wells
With Tailing
If No Tailing
Source: Chapman and Parker, 2005 Copyright 2005 American Geophysical Union. Reproduced/modified by permission of AGU.
25
Notes: RITS Spring 2008: Dilute Groundwater Plume Management
25

## Slide 27
Matrix Diffusion Background
Lines of Evidence
New Conceptual Model
Collecting Field Samples
Mini Road Map

## Slide 28
Sale et al., 2008
Life Cycle of a Chlorinated Solvent Site
Early Stage
27
Notes: 27

## Slide 29
Sale et al., 2008
Middle Stage
28
Life Cycle of a Chlorinated Solvent Site
Notes: 28

## Slide 30
Sale et al., 2008
Late Stage
29
Life Cycle of a Chlorinated Solvent Site
Notes: 29

## Slide 31
EARLY STAGE
Early Stage
1s
10s
100s
>1,000s
GW. or equivalent GW. conc.
30

## Slide 32
MIDDLE STAGE
Middle Stage
1s
10s
100s
>1,000s
GW. or equivalent GW. conc.
31

## Slide 33
Late Stage
1s
10s
100s
>1,000s
GW. or equivalent GW. conc.
32

## Slide 34
MD Toolkit Does This…
1s
10s
100s
>1,000s
GW. or equivalent GW. conc.
OR
33

## Slide 35
Matrix Diffusion Background
Lines of Evidence
New Conceptual Model
Collecting Field Samples
Mini Road Map

## Slide 36: High-Resolution Soil Core Subsampling
Sorbed
mass
Dissolved
mass
Soil core
Sample
volume
Guilbeault, 1999
Subsample in
pre-weighed
vial with MeOH
Stainless steel
sampler (3/4” ID)
0
4 in
plunger
35
Notes: 35

## Slide 37: Field Sampling Step 1. Real-time Profiling to Identify Intervals of Interest
Index of Hydraulic Conductivity (Ik)
Contaminant concentration and physical-chemical properties through GW sample collection
Ik
GW conc.
Low K silt
36
Several tools available, including WaterlooAPS (from Stone Environmental Inc.)

## Slide 38: Step 2. Soil Subsampling
Core contained in
aluminum tube or other liner
Splitting core tube lengthwise
2”
Half of core wrapped in foil to minimize volatilization
Subsampling for VOC analyses: sub-sample placed in
pre-weighed vial with MeOH
[TCE] (mg/g wet soil)
Depth (ft bgs)
Interface
CH-2 Downgradient Area
Obtain several high-resolution soil profiles per site
37

## Slide 39: Constant Loading vs. Declining Aquifer Concentration
Zone with DNAPL
Downgradient of Isolated Source
Chapman and Parker, 2005

## Slide 40
Diffusion Curves
t
N U M B E R 1
Exercise
39
Notes: 39
39
39

## Slide 41: Match the Curves

## Slide 42: Match the Curves - Answers

## Slide 43
Analytical groundwater model that estimates source concentration over time, i.e., a “source history”
WHAT:
Modeling Historical Impacts –
Source History Tool
Free download from:
http://www.serdp.org (soon)
http://www.gsi-net.com (now)
WHERE:
WHO:
S. Farhat, P. de Blanc, C. Newell, and D. Adamson
GSI Environmental Inc.
Project Team: B. Parker and
S. Chapman
University of Guelph
T. Sale
Colorado State University
Funded by ESTCP
(ER-201032)
Notes: 42
42
42

## Slide 44
Introduction
Matrix Diffusion Background
Options for Modeling Matrix Diffusion
Introduction to MDT – Square Root Model
Dandy-Sale Model in the MDT
Case Study 1
Case Study 2
Wrap-up
Road Map

## Slide 45
Types of Groundwater Models
Flow vs. Transport Models
Analytical Models
Numerical Models
44

## Slide 46
Numerical Models: It takes a lot of grid cells to model this….
(Chapman, Sale, Doner, Parker, 2012)
~25,000 elements
~7,500 elements
~10,000 nodes
45

## Slide 47
46
“Square Root” “Dandy-Sale”
REMChlor
Three Simple Analytical Matrix Diffusion Models

## Slide 48
REMChlor and REMFuel
Source/Plume/Remediation Models
But no matrix diffusion
In the plume
Matrix Diffusion in Source
Source
Falta et al., 2007
Plume
Flow
47
You enter source mass, concentration leaving source
You decide how mass leaves over time with “gamma”
A high gamma (>1.0) can simulate matrix diffusion
Notes: 47
47
47

## Slide 49
REMChlor Model – Effect of Gamma
Can simulate matrix diffusion in source, but not plume…
Gamma > 1.0 Gives “long tail” in source similar to matrix diffusion
Gamma = 1.0
Gamma = 0.5
Gamma = 2.0
Notes: 48
48
48

## Slide 50: “Square Root Model” for Matrix Diffusion
“On-Off” Source
Dr. Tom Sale
Dr. Tissa Illangasekare
Adapted from
Parker et al., 1995
49
Notes: 49

## Slide 51: “Square Root” Matrix Diffusion Model
MD: Mass Discharge from Low Perm. Unit (grams per day) assuming no concentration in transmissive zone
ϕLP - Low Permeability Unit Porosity
De - Effective Diffusion Coefficient of Low Perm Unit,
R - Retardation Factor of Low Perm Unit
t - Time Loading Started, years before simulation time
t’ - Time Loading was Removed, years before simulation time
Cs - Concentration at interface during loading period
50

## Slide 52
MEW Site
Mountain View, California
51
Team members: Schlumberger, GSI, Geosyntec
  Seyedabbasi et al., Remediation, 2013
  McDade et al., Remediation, 2013

## Slide 53
MEW Site: Site Hydrogeology
Source: Geosyntec
52

## Slide 54
Middlefield–Ellis–Whisman Site
Three Zones: A/A1, B1/A2, B2
1980s: Slurry Walls, Pump & Treat
Today ~100 recovery wells, ~500 gpm
Removal: ~97,000 pounds VOCs
Reduction: Approximately 1 OoM decrease in average TCE concentration 1992-2009
Pump & Treat System at MEW Site
53

## Slide 55
Example A: MEW Site Pump and Treat Capture Zones
Pumping Well
Ground-
water Flowline
54

## Slide 56
Matrix Diffusion Model Applied to MEW Site
“Charging Period”
“Back Diffusion Period”
Then Build Slurry Walls, P&T Wells, Contain Sources
55

## Slide 57
Chart: Date
| 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009
Observed | 6.4259 | 17.0231 | 16.0648 | 14.8811 | 13.8665 | 9.4698 | 8.4552 | 8.117 | 8.117 | 6.4259 | 7.1024 | 5.4113
Flushing with Pore Volume Model | 10.3136 | 0.65586 | 0.010117 | 0.00032091 | 1.1065e-05 | 3.0867e-07 | 1.2517e-08 | 5.3176e-10
Matrix Diffusion Model
Flushing/Retardation
Model
Results: Recovery Well REG-8A: 30 Pore Volumes
56
Notes: 56

## Slide 58: Dandy-Sale Model
Sale, Zimbron, Dandy, 2008
57
Loads up the low perm zone, then release period
Vertical Plane Source
(Higher concentration near bottom)

## Slide 59: Dandy-Sale Analytical Matrix Diffusion Model
58

## Slide 60
59
1. REMChlor | 2. Square Root Model | 3. Dandy-Sale Model
Simple | Very simple | Complex Function
Vertical plane source | Horizontal source is directly over low perm zone | Vertical plane source upgradient of low perm zone
No matrix diffusion in plume | On-off source Unimpeded back diffusion | On-off source More accurate back diffusion
Concentration or Mass Discharge | Mass discharge Mass in low perm Concentration in Well | Same as Square Root, but with Conc. in Low Perm.
U.S. EPA CSMoS (Google: “EPA” and “REMChlor”) | ESTCP Matrix Diffusion Toolkit (www.gsi-net.com) | 
59

## Slide 61
Introduction
Matrix Diffusion Background
Options for Modeling Matrix Diffusion
Introduction to MDT – Square Root Model
Dandy-Sale Model in the MDT
Case Study 1
Case Study 2
Wrap-up
Road Map

## Slide 62
Analytical groundwater transport models that estimates matrix diffusion effects
WHAT:
Free download from:
http://www.serdp.org
http://www.gsi-net.com
WHERE:
Matrix Diffusion Toolkit
WHO:
S. Farhat and C. Newell
GSI Environmental Inc.
T. Sale, D. Dandy, and
J. Wahlberg Colorado State University
Funded by ESTCP
Notes: 61
61
61

## Slide 63
Header #2
Square Root Model: Data Input Screen
62

## Slide 64
Select “Source Zone Analysis” to see matrix diffusion impacts in a source zone:
Select “Plume Analysis” to see matrix diffusion impacts in a downgradient plume:
Select “PRB Analysis” to see matrix diffusion impacts downgradient of a PRB:
63

## Slide 65
Parameter | Description
Low-k Zone Description | Choose from dropdown menu or enter directly
Low-k Zone Total Porosity | Keep Toolkit default or enter directly. Based on Pankow and Cherry (1996) Domenico and Schwartz (1999) Davis (1969) and Johnson and Morris (1962)
Transmissive Zone Darcy Velocity | Enter directly or use Toolkit to calculate
64

## Slide 66
Parameter | Description
Molecular Diffusion Coefficient in Free Water | Keep Toolkit default or enter directly From TRRP (2008) TCE = 9.1E-06 cm2/s PCE = 8.2E-06 cm2/s Benzene = 9.8E-06 cm2/s Other refs: Pankow and Cherry (1996), Wiedemeier et al. (1999), etc.
Square Root Model: Transport
65

## Slide 67
Parameter | Description
Apparent Tortuosity Factor Exponent | Keep Toolkit default or enter directly
Apparent Tortuosity Factor Exponent
66
tortuosity
porosity
 = np
p varies:
  1/3: Millington, 1959
  0.3 to 1.5: Charbeneau, 2000
  1.3 to 4.5: Pankow and Cherry, 1997
  0.33 for Clay: Parker et al., 1994

## Slide 68: GSI’s Decision Support for Tortuosity
(1) Pick Material
If no porosity value is entered:
Default Porosity
Tortuosity factor
If porosity value is entered:
Tortuosity factor
Gravel
Sand
Silt
Clay
Sandstone/Shale
Granite
(2) Software Produces
67

## Slide 69
Soil Type | Default Porosity | Relationship* | Estimated Tortuosity
Fine Sand | 0.20 | t = n0.33 | 0.59
Silt | 0.48 | t = n1.1 | 0.45
Clay | 0.47 | t = n1.1 | 0.44
Sandstone/ Shale | 0.10 | t = n | 0.10
Granite | 0.006 | t = n0.55 | 0.06
Current Look-up Table
68
* From Parker et al. (2004); Millington and Quirk (1961); and Pankow and Cherry (1996)

## Slide 70
69
Parameter | Description
Retardation Factor | Enter directly or use Toolkit to calculate Transmissive zones 1-3 (typical for BTEX) 2-5 (typical for CVOC) Low-k zones Thought to be > trans zones. Currently, few sites with data
Retardation Factor

## Slide 71
Calculating Retardation Factor
Parameter | Description
Koc | Keep Toolkit default or enter directly From TRRP (2008) TCE = 93 mL/g PCE = 155 mL/g Benzene = 66 mL/g Other refs: Pankow and Cherry (1996), Wiedemeier et al. (1999), etc.
70

## Slide 72
Calculating Retardation Factor Cont’d
71
Parameter | Description
Low-k zone fraction organic carbon | Enter directly Likely range: 0.0002 - 0.10 Chapman and Parker (2005): silts and clays = 0.0024 to 0.00104 Adamson (2012): clay = 0.001; silts = <0.0005 to 0.0022
Soil bulk density of low-k zone | Enter directly Typical value = 1.7 g/mL Lovanh et al. (2000) and Domenico and Schwartz (1990): Clay = 1.0 to 2.4 Sandstone = 1.6 to 2.68 Koerner (1984): Stiff glacial clay = 2.07 organic clay = 1.43

## Slide 73
Square Root Model: Plume Charac.
50
500
5000
5
72

## Slide 74
Plume Characteristics Cont’d
50
500
5000
5
73

## Slide 75
74
50
500
5000
5

## Slide 76
Square Root Model: General
75

## Slide 77
Square Root Model: Field Data
Can enter up to 8 values for comparison
  Helps with model calibration
76

## Slide 78
Mass discharge
SRM Output
Concentration in transmissive zone
Mass in low-k zone
SRM = Square Root Model
77

## Slide 79
Introduction
Matrix Diffusion Background
Options for Modeling Matrix Diffusion
Introduction to MDT – Square Root Model
Dandy-Sale Model in the MDT
Case Study 1
Case Study 2
Wrap-up
Road Map

## Slide 80
Dandy-Sale Model: Data Input Screen
79

## Slide 81
Dandy-Sale Model: Hydrogeology
Similar to SRM Data Input
  Choose from dropdown menu or enter directly
  Keep Toolkit default or overwrite
  Enter directly or use Toolkit to calculate value
80

## Slide 82
Dandy-Sale Model: General
81

## Slide 83
Dandy-Sale Model: Outputs
82
Low-k Zone
  2-D aqueous concentration
  Aqueous concentration vs. distance
  Aqueous concentration vs. depth
  2-D sorbed concentration
  2-D total concentration
Transmissive Zone
  Aqueous concentration
  Mass discharge
  Sorbed concentration
  Total concentration
Aqueous, Sorbed, and Total Mass
  Low-k zone
  Transmissive zone

## Slide 84
Introduction
Matrix Diffusion Background
Options for Modeling Matrix Diffusion
Introduction to MDT – Square Root Model
Dandy-Sale Model in the MDT
Case Study 1
Case Study 2
Wrap-up
Road Map

## Slide 85
84

## Slide 86
Case Study #1: Industrial Site, CT
  Metal product manufacturing site (1952 – 2001)
  TCE occurs in surficial sandy aquifer
    overlying a clayey silt aquitard
  TCE DNAPL isolated in 1994 using steel sheet pile enclosure
  Historical industrial pumping resulted in a long-term downward hydraulic gradient across the aquitard
  In 2000, TCE observed in
    Vertical cores collected from aquitard below plume
    Depth-discrete multilevel sampling
Site from Chapman and Parker, 2005
85

## Slide 87
Case Study #1: Industrial Site, CT
86
Matrix Diffusion Toolkit used to:
  Estimate effects of diffusion into and from low-k zones
  Both SRM and DSM applied
    Step 1: Initial values entered into the Toolkit
    Step 2: Toolkit outputs compared to field observed TCE

## Slide 88
Parameter | Value
Low-k porosity | 0.43
Darcy velocity | 0.13 m/d
Retardation factor | 1.2
Representative concentration | 37,000 ug/L (max observed)
Conc. zone dimensions | 330 m x 300 m
Source starts | 1952
Source removed | 1996 (“effective”)
Mol. Diff. coeff. (Toolkit default) | 9.1 x 10-10 m2/sec
App. tort. fac. exp. | 0.42
SRM: Site-specific Parameters
87

## Slide 89
SRM: Input Screen
88

## Slide 90
SRM: Concentration Output
89

## Slide 91
SRM: Mass in Low-k Zone
90

## Slide 92
SRM: Output
Estimate of Time to Clean
  > 500 years to reach MCL of 5 ug/L
91

## Slide 93
Case Study #1: SRM Key Points
MCL = Maximum Contaminant Level
92
Matrix Diffusion Toolkit reproduced observed concentrations within an order of magnitude
No adjustment needed for Toolkit default parameters
Matrix Diffusion Toolkit reproduced observed mass in low-k zone within an order of magnitude
SRM modeling estimates >500 yr to reach MCL of 5 ug/L
  Compares well to Chapman and Parker’s more sophisticated modeling that indicated concentrations “will remain much above the MCL for centuries.”
Typical advection-dispersion type model would show no mass in the low-k unit, a fundamentally incorrect conceptual model

## Slide 94
Introduction
Matrix Diffusion Background
Options for Modeling Matrix Diffusion
Introduction to MDT – Square Root Model
Dandy-Sale Model in the MDT
Case Study 1
Case Study 2
Wrap-up
Road Map

## Slide 95
94
Case Study #2: DSM Modeling
Same site as Case Study #1
DSM used to estimate effects of diffusion into and from low-k zones
Estimate groundwater concentrations in the low-k zone
  Source area
  Plume area
Modeling approach:
  Step 1: Initial values entered into the Toolkit
  Step 2: Toolkit outputs compared to field observed TCE values

## Slide 96
Parameter | Value
Low-k (silt) porosity | 0.43
Trans zone (sand) porosity | 0.35
Seepage velocity | 0.37 m/d
Mean concentration | 1100 mg/L (TCE solubility)
Trans zone bulk density | 1.7 g/mL
Low-k zone bulk density | 1.5 g/mL
DSM: Site-specific Parameters
95

## Slide 97
Parameter | Value
Trans zone foc | 0.038%
Low-k zone foc | 0.054%
Conc. zone dimensions | 32 m x 39 m
Source starts | 1952
Source removed | 1997
foc = fraction organic carbon
DSM: Site-specific Parameters
96

## Slide 98
Parameter | Value
Mol. diff. coeff. | 9.1 x 10-10 m2/sec
Trans zone app. tort. fac. exp. | 0.33
Low-k zone app. tort. fac. exp. | 0.42
Organic carbon part. coeff. | 93.3 L/kg
Coeff. Transverse hyd. disp | 0.16
DSM: Toolkit Default Parameters
97

## Slide 99
Source Evaluation
98

## Slide 100
Comparison of DSM with Observed
99

## Slide 101
Matrix Diffusion Toolkit reproduced observed concentrations reasonably well
Comparison using max reported source concentration of 1300 mg/L
  Also reproduced observed concentrations reasonably well
No adjustment needed for Toolkit default parameters
Case Study #2: Key Points
100

## Slide 102
Future Predictions
101
2020
2030
Concentration in low-k zone
Concentration in low-k zone
Lateral Distance from Source
Lateral Distance from Source

## Slide 103
Introduction
Matrix Diffusion Background
Options for Modeling Matrix Diffusion
Introduction to MDT – Square Root Model
Dandy-Sale Model in the MDT
Case Study 1
Case Study 2
Wrap-up
Road Map

## Slide 104
I Want the Following Information: | Which Model? | Output
1. Mass Discharge (sometimes called mass flux) data from a low-k zone to a transmissive zone in units of grams per day versus time (both past and future). | Square Root OR Dandy-Sale | Mass discharge vs. time plot
2. How much mass could be present in low-k zones at my site? | Square Root OR Dandy-Sale | Mass in low-k zone vs. time plot
Which model should I use: SRM or DSM?
103

## Slide 105
I Want the Following Information: | Which Model? | Output
3. If I install a permeable reactive barrier, will I have trouble achieving downgradient cleanup standards? | Square Root OR Dandy-Sale | Concentration* vs. time plot or mass discharge vs. time plot
4. I want to know the concentration vs. depth profile in a low-k zone. | Dandy-Sale | Concentration* vs. depth plot or Concentration vs lateral distance plot
Which model should I use: SRM or DSM?
* Concentration assuming a monitoring well with a 10-foot screened interval (this cannot be changed in the model)
104

## Slide 106
I Want the Following Information: | Which Model? | Output
5. If I remove all the DNAPL in a source zone, is there a chance I’ll still be above MCLs? How much longer might I have to wait for a source zone to achieve MCLs after the DNAPL is all gone? | Dandy-Sale | Concentration* vs. time plot or mass discharge vs. time plot
* Concentration assuming a monitoring well with a 10-foot screened interval (this cannot be changed in the model)
105
Which model should I use: SRM or DSM?

## Slide 107
I Want the Following Information: | Which Model? | Output
6. I want to make sure the matrix diffusion model accounts for contaminant concentrations in the transmissive zone when calculating the release for low-k zones? | Dandy-Sale | Concentration* vs. time plot or mass discharge vs. time plot
* Concentration assuming a monitoring well with a 10-foot screened interval (this cannot be changed in the model)
106
Which model should I use: SRM or DSM?

## Slide 108
I Want the Following Information: | Which Model? | Output
7. I want to account for the travel time of the plume in the transmissive zone so that the loading period for the downgradient low-k zones starts later than the loading period for the near-source low-k zones. (This is more important for plumes, such as plumes with long residence times, > 20 years). | Dandy-Sale | Concentration* vs. time plot or mass discharge vs. time plot
* Concentration assuming a monitoring well with a 10-foot screened interval (this cannot be changed in the model)
107
Which model should I use: SRM or DSM?

## Slide 109
Model Demo