## Slide 1: Site Cleanup Remedial Investigation Summary
  Remedial Investigation (RI) / Feasibility Study (FS) Work Plan
    RI to be conducted in three phases
      Three individual field sampling events (Steps 1 though 3)
    Investigation conducted from 2005 to 2010
      Step 1 included background and area of concern (AOC) surface soil sampling, sediment/surface water sampling, and development of conceptual site model (CSM)
      Step 2 included initial groundwater investigation and additional surface water delineation
      Step 3 included horizontal extent of groundwater impacts
  Final RI Report including Human Health and Baseline Ecological Risk Assessments submitted in June 2011

## Slide 2: Site Cleanup Remedial Investigation Summary
  Areas of Concern (AOC)
    AOC #1 – West Tailings Impoundment
    AOC #2 – North Tailing Impoundment
    AOC #3 – Former Mill Buildings (Tailings/Pyrite Storage)
    AOC #4 – Mine Pit Pond (MPP)
    AOC #5 – East Tailings Impoundment
    AOC #6 – Surface Water
    AOC #7 – Random Dumping Areas
    AOC #8 – Waste Rock (North)
    AOC #9 – Waste Rock (South)
    AOC #10 – Site Groundwater
1
2
3
4
5
6
8
9

## Slide 3: Site Cleanup Remedial Investigation Summary
  RI Environmental Sampling
    surface soil samples
    surface water samples
    sediment samples
    monitoring wells/piezometers
    residential well samples
    ecological samples
  Post-RI Environmental Sampling
    surface and subsurface soil samples
    test pits
    whole rock samples
    monitoring wells/piezometers
    residential well samples
    groundwater sampling events

## Slide 4: Site Cleanup Remedial Investigation Conclusions
  Soils
    No statistical difference between background metals in soils collected from mineralized zone (ore body outcrops) and non-mineralized zone
    Acid Base Accounting (ABA) and paste pH from AOC surface soil samples indicates capacity to produce acid mine drainage (AMD)
    Aluminum, iron, and manganese are not particularly elevated in the AOCs when compared to background soils
    No unacceptable risk to human health or ecological receptors
  Sediment
    No unacceptable risk to human health or ecological receptors by sediment
  Surface Water (MPP)
    Surface water in MPP has minimal hydraulic connection with the underlying bedrock and primarily only along strike of ore body
    Impact to pond water results from acid rock drainage (ARD)

## Slide 5: Site Cleanup Remedial Investigation Conclusions
  Surface Water (Tributaries)
    AMD impacts associated with leaching from tailings to groundwater generally restricted to headwaters of tributaries
    pH and concentrations of metals generally improve downstream
    No unacceptable risk to human health by exposure to surface water
    Ecological condition of concern for surface water is low pH and acidity
  Groundwater
    Groundwater is the primary source of potable water in the site area
    Groundwater is present under water table conditions in both overburden soils formed by the in-place weathering of bedrock and in fractured bedrock
    Groundwater in site area has relatively low pH (less than 7) and may have elevated metals due to geology, as a result of ARD
    Groundwater in monitoring wells installed downgradient from tailings impoundments have very low pH and are impacted by AMD

## Slide 6: Site Cleanup Remedial Investigation Conclusions
  Groundwater
    Based on age of site, history of operations, and release mechanisms, the magnitude and extent of impacts to groundwater are expected to be stable in the future
    The boundary of groundwater affected by the site appears stable and should not expand, but is expected to persist
    Non-cancer risk to future use of groundwater as a potable water source due to elevated metals, primarily cobalt and manganese
      Risk is associated with hypothetical exposure to the highest concentrations of metals reported in site monitoring wells and doesn’t represent risks associated with current use of groundwater as a potable drinking water supply
      Remedial action objective developed to prevent use of groundwater that contains concentration of metals that pose non-cancer risks to human health
    Due to abundant metals present in geological formations in site area, it’s difficult to differentiate between AMD-impacted groundwater and naturally occuring groundwater impacted by ARD

## Slide 7: Site Cleanup AMD-Impacted vs ARD-Impacted Groundwater
  AMD is a common environmental impact at former mining sites where iron sulfide minerals (principally pyrite) are present and exposed to water and oxygen, releasing sulfate, iron, and acidity (H+)
    A simplistic, overall chemical formula that results in AMD is:
          Pyrite + Oxygen + Water → Iron Precipitates + Acidity
    Acidic waters also promote the weathering of other minerals
    Mining and benefication of the ore body resulted in the accumulation of mine residuals in the form of fine-grained tailings and waste rock piles
      Fine-grained materials, such as tailings, will result in higher oxidation rates due simply to increased surface areas of pyrite exposed to oxygen and water
      The ability of the tailings to continue to produce acid and leach metals is limited only by the presence and amount of pyrite, soluble salts, oxygen, and the availability of water in the form of infiltrating precipitation
      Acid Base Accounting (ABA) analysis and paste pH sampling indicated that tailings are a source of AMD, however, waste rock is not a significant source of AMD

## Slide 8: Site Cleanup AMD-Impacted vs ARD-Impacted Groundwater
  Similar acid weathering conditions occur in the absence of mining operations and is commonly called ARD
    Oxidation of pyrite from in-place bedrock, most notably between the water table and the land surface
    Increasingly recognized environmental condition at construction sites, transportation corridors, and other areas where bedrock is excavated
    Evidence of ARD, including exposed outcrops with weathered sulfide minerals and anomalously elevated metals in stream sediments, are all tools used by the mineral exploration geologist to locate sulfide-bearing mineral deposits
    ARD can an occur in potable wells installed in sulfide-bearing bedrock when oxygen is introduced through the well installation and subsequent pumping
    ARD has been encountered in private wells along the strike of the ore body as well as along Pat’s Road located along strike of an unmined northwestern kyanite quartzite formation that parallels the ore body at Henry Knob

## Slide 9: Site Cleanup AMD-Impacted vs ARD-Impacted Groundwater

## Slide 10: Site Cleanup AMD-Impacted vs ARD-Impacted Groundwater
  The area around Henry Knob has a remarkable diversity of rock formations and mineral resources
    Unusual in the richness and variety of the mineral deposits that they contain
      Mineral deposits include, among others, kyanite and manganese
      It has been estimated that the principal deposits in the region contain 40 million tons of rock with 10 to 30 percent kyanite
      The most significant mining in the area was at Henry Knob, where kyanite was produced with pyrite as a byproduct
    Mining has played a significant role from the 1700s to the present
  How do we differentiate between groundwater impacted by AMD and naturally-occurring groundwater that may have elevated concentrations of metals, but otherwise no impacts from mining operations?

## Slide 11: Site Cleanup AMD-Impacted vs ARD-Impacted Groundwater
  To differentiate between naturally-occurring metals in groundwater and groundwater that has likely been impacted by AMD, a combination of geochemical signature (Stiff diagrams) and risk-based screening levels was developed
  Both monitoring wells and residential wells were sampled for geochemical parameters that could be used to determine if the samples showed impact from AMD
  The geochemical parameters consisted of major anions (bicarbonate, chloride, and sulfate), major cations (calcium, magnesium, sodium, and potassium), ferrous iron, ferric iron, sulfide, acidity, and total alkalinity
  Analyte composition and anion-cation balances for these geochemical parameters were used to generate Stiff diagrams

## Slide 12: Site Cleanup AMD-Impacted vs ARD-Impacted Groundwater
  Stiff diagrams are used to describe and compare geochemical differences in groundwater based on charge balances of the cation and anion species by calculating and plotting equivalent charge concentrations in milliequivalents per liter (meq/L)
    A polygonal shape is created from three parallel horizontal axes extending on either side of a vertical zero axis
    Cations are plotted on the left side of the zero axis, one to each horizontal axis, and anions are plotted on the right side

## Slide 13: Site Cleanup AMD-Impacted vs ARD-Impacted Groundwater
  The geochemical signature of mine-impacted groundwater indicates a charge imbalance that is skewed toward high sulfate concentrations (relative to the cations) and depleted bicarbonate (due to acidity) consistent with geochemical processes responsible for AMD
  Where the pennant shape of the Stiff diagram was not observed, the groundwater was interpreted to not have been impacted by AMD

## Slide 14: Site Cleanup AMD-Impacted vs ARD-Impacted Groundwater
  Patterns in the Stiff diagrams are useful in making a rapid visual comparison of geochemical data and allows discrimination between water from different sources

## Slide 15: Site Cleanup AMD-Impacted vs ARD-Impacted Groundwater
  Metals were detected in groundwater from the overburden monitoring wells (saprolite), bedrock monitoring wells, and residential water supply wells (most are assumed to be installed in bedrock) at the Site
  Although aluminum, cobalt, and manganese were detected with the most frequency at the site, manganese was the most widespread constituent that exceeded the USEPA Regional Screening Level (RSL) in effect at the time of the RI
  A concentration contour approximately equivalent to the USEPA RSL for manganese was used in conjunction with Stiff diagrams to develop the extent of AMD-impacted groundwater
  Groundwater sample results that exceed the USEPA RSL but do not have Stiff diagrams indicative of AMD were not included within the manganese-impacted groundwater concentration contours

## Slide 16: Site Cleanup AMD-Impacted vs ARD-Impacted Groundwater
  Figure from RI demonstrating area of groundwater potentially impacted by mining operations
    Solid red line indicates boundary of potentially AMD-impacted groundwater based on Stiff diagrams combined with manganese concentrations above the USEPA RSL in effect at the time of the RI
    Dashed purple line indicates a manganese concentration contour approximately equivalent to the USEPA RSL

## Slide 17: Site Cleanup Regional/Telescoped Groundwater Model
  Regional 3D flow model developed using MODFLOW with data input, model runs, and model output using MT3E code in Processing Modflow
    Assess potential impacts of dissolved metals (cobalt and manganese) on regional groundwater quality in site area
    Further refine CSM
  Telescoped model performed using 3D reactive transport code PHT3D
    Simulate future transport of low pH groundwater and evaluate groundwater impact to surface water bodies
      ARD/AMD simulated through oxidation of pyrite
      Subsequent pH reactive transport determined by site-specific geochemical conditions
    Evaluate effectiveness of remedial alternatives
      Monitored natural attenuation (MNA)
      Impermeable cap over tailings
      Vegetative cap over tailings
      Excavation with off-site disposal
      Excavation with on-site disposal (MPP)

## Slide 18: Site Cleanup Regional/Telescoped Groundwater Model
  Regional 3D flow model, due to high soil/water partitioning coefficient (Kd) for cobalt and manganese, demonstrated no significant plume migration over 30-year modeling period

## Slide 19: Site Cleanup Regional/Telescoped Groundwater Model
  Telescoped models demonstrated pH distribution over the 30-year modeling period for each simulated remedial alternative
  Most of impacts noted in Layer 1 (shallow) of model (generally equivalent to overburden)

## Slide 20: Site Cleanup Regional/Telescoped Groundwater Model
  No significant changes in pH for MNA alternative
  No significant changes in pH for impermeable cap alternative
  Significant improvement in pH over the 30-year modeling period for vegetative cap and excavation alternatives
    Due to the relatively high costs for excavation/disposal of the tailings and the increased risk due to vehicular traffic, the installation of a vegetative cover was considered the more feasible alternative
    Additional model runs performed to simulate buffering of the water in the MPP indicated some pH improvement, but not enough to overcome the ARD generated from the geology of and surrounding the MPP

## Slide 21: Site Cleanup Regional/Telescoped Groundwater Model
  Vegetative Cover

## Slide 22: Site Cleanup Groundwater Monitoring Program
  Initiated in June 2015
  Objectives
    Monitor groundwater plume stability in impacted area
    Monitor surface water concentrations trends over time
    Monitor effectiveness of treatments systems installed as part of Non-Time Critical Removal Action (NTCRA)
  Term
    Conduct trend analysis on each monitoring point following completion of baseline sampling
    Once trend analysis shows metals concentrations are stable or deceasing, monitoring will be terminated

## Slide 23: Site Cleanup Groundwater Monitoring Program
  Locations monitored in the program
    Bounding wells (defines the extent of groundwater impacted by AMD)
      7 overburden monitoring wells and 6 bedrock monitoring wells
      8 private water supply wells
    Interior wells (within area of AMD-impacted groundwater)
      9 overburden monitoring wells and 5 bedrock monitoring wells
      40 private water supply wells
    Surface water locations
      Headwaters of West Tributary, East Tributary, and Allison Creek Tributary
      MPP
  Baseline Sampling
    All wells and surface water locations
    Quarterly for two years
    Baseline completed in first quarter of 2017

## Slide 24: Site Cleanup Groundwater Monitoring Program
  Subsequent Sampling
    Bounding monitoring wells, bounding private wells, interior monitoring wells, and interior private wells with metals concentrations below the Remedial Goals (RG) sampled annually
    Interior wells with metals concentrations above the RG sampled semi-annually
  Problems encountered due to lack of access
    15 private wells (3 bounding and 12 interior) could not be sampled due to lack of access from owner
    Access obtained for 13 of the 15 wells in second/third quarters of 2017
      Wells will be sampled quarterly for two years unless otherwise abandoned
      Remaining two wells will not be sampled due to continued lack of access from property owners

## Slide 25: Site Cleanup Groundwater Monitoring Program
  Trend Analyses
    Bounding Wells
      Decreasing cobalt concentrations in overburden, bedrock, and private wells
      Decreasing manganese concentrations overburden wells
      Decreasing manganese concentrations in over half of bedrock and private wells
      Wells with increasing manganese concentrations have relatively neutral pH (not indicative of AMD), are significantly below RG for manganese and in many cases, below the secondary maximum contaminant level (SMCL) for manganese
    Interior Wells
      Generally decreasing trends for cobalt except where evidence of AMD-impacts noted
      Generally decreasing trends for manganese