## Slide 1: Soil Treatment at the California Gulch NPL Site for Vegetation Reestablishment and Mitigation of Metal Mobility
Stuart Jennings, RRG, Jan Christner, URS
Mike Holmes, EPA and John DeAngelis, PWT

## Slide 2: Operable Unit 11 of the California Gulch Superfund Site near Leadville, CO

## Slide 3
Pre-Treatment (~2008)
Post Treatment (~2010)

## Slide 4: Irrigated Meadows
Before remediation
After remediation
Notes: Arrow is provided for reference—the same spot in both photos

## Slide 5: Arkansas River Fluvial Tailing Areas
Fluvial Tailing Deposits
Unstable Streambanks

## Slide 6: Prior Research and Demonstration Work
1999 EPA Demonstration
University Research
Harry Compton (EPA), Mark Sprenger, (EPA), Sally Brown (USDA/UW), Mike Zimmerman (EPA), Jan Christner (URS)
CSU Revegetation Research
Kevin Fisher, MS 1999
Joe Brummer, principal investigator
Notes: Lime and no-lime differences shown in left photo, Low and High phosphorous amendment shown in right photo

## Slide 7: Two Treatment Strategies
Irrigated Meadow Contamination
153 acres treated to either 6 or 12 inch depth using a tractor-pulled plow
Thin deposits of relatively uniform depth
Fluvial Tailing Deposits
18 acres treated with an excavator-mounted soil mixer
Thick deposits of varying depths within the floodplain
Notes: The amendment rates will vary by type and probably within each type. While the overall approach is similar—using soil amendments mixed into the contaminated media—each approach will be unique and adapted to the specific site reflecting soil rock content, depth to groundwater, soil pH, lime requirement, proximity to streambanks, presence or absence of existing woody vegetation, post-treatment land use, etc.

## Slide 8: Remedial Action Objectives
Minimize future human exposures
Minimize erosion
Control leaching and migration of metals
Reduce toxins in plants
Reduce metal exposures of wildlife and livestock
1990’s-2006—Data Collection, Research, Demonstration
2007—Work plan
2008-2009—Construction
2010-present—Monitoring and maintenance
Remedial Timeline

## Slide 9: Soil Treatment
Approach
Add lime to control current and future acidity
Add organic amendment to serve as basis for long-term soil fertility/nutrient cycling
Add supplemental phosphorous
Treat entire contamination thickness
Seed
Monitor and maintain
Expected Outcome
Soil pH will remain between 7-8 and control soluble metals
Nutrient cycling will be perpetuated by soil organisms
Vegetation will not translocate harmful concentrations of contaminants into shoots
Water balance will be improved
  Reduced metal flux to groundwater
  Reduced runoff/reduced erosion
  Increased evapotranspiration
Conventional land uses will be restored (grazing and recreation)
Meet RAO’s and Performance Standards
Notes: Mention companion poster related to performance standards

## Slide 10: Soil Treatment Polygons— Irrigated Meadows North
12-inch tillage --Pink coded polygons
6-inch tillage – Yellow coded polygons

## Slide 12: Lime Amendment Mixing into Fluvial Tailing Deposits
Notes: Poster Presentation on Project Construction

## Slide 13: Lime Requirement for Soil Treatment

## Slide 14: Sugar Beet Lime
13,000 tons used for project

## Slide 16: Compost Amendment
28,000 tons used for project (45,000 cy)

## Slide 17: Soil Total Metal Levels (2011) Post-Treatment
RESULTS
Elevate metal levels and essentially
unchanged from pre-treatment

## Slide 18: Changes in SPLP Soluble Metal Levels Before and After Treatment
Post-Treatment Comparisons between Totals and Water Soluble levels | Pb | Zn
Water soluble as a percent of total | 0.022% | 0.065%
Total as a factor of soluble | 4588X | 1543X
Notes: SPLP - Synthetic Precipitation Leaching Procedure
A prominent reduction in metal mobility after treatment

## Slide 19: Soil Conditions
Soil pH and Electrical Conductivity
Acidic prior to treatment
Neutral to slightly alkaline following lime addition (7-8)
Soil solution dominated by metals prior to treatment
Soil solution dominated by alkaline cations and nutrients following treatment
Soil Organic Matter
and Fertility
Prior to treatment organic matter varied widely from near zero (bare areas) to adequate (sparse areas)
Prior to treatment plant macronutrients N/P/K were deficient in nearly all barren/sparsely vegetated areas
Following treatment adequate to abundant fertility levels were observed

## Slide 20: Lead levels in Vegetation
The amount of Pb in vegetation appears unrelated to total Pb in soil. Differences are apparent by site.

## Slide 21: Lead levels in Vegetation
Water soluble Pb also appears to be a poor predictor of Pb in vegetation.

## Slide 22: Lead levels in Vegetation
SPLP soluble Pb appears to provide good discrimination of Pb in vegetation by site location

## Slide 23: 2011 Vegetation Monitoring
Fluvial Deposit QF
Irrigated Meadow SM-06
Total Metal Levels (mg/kg) |  | 
 | Pb | Zn
QF | 988 | 1310
SM-06 | 4900 | 5060
Notes: Red arrow points to the same willow

## Slide 24: June 2009
July 2009
November 2009
July 2010
October 2010
July 2010
Fluvial Deposit QF

## Slide 25: On-going Maintenance
Streambank Repairs due to High Flow in 2011
Reseeding Bare Spots caused by Excess Salinity

## Slide 26: On-going Management
Grazing Intensity
Weed Control

## Slide 27: Remediation and Stabilization Using Natural Materials
Lime
Compost
Local Borrow Soil and Rock

## Slide 28: Remediation and Stabilization Using Natural Materials
Carex
Willows

## Slide 29: Soil Treatment and Vegetation Trends— Arkansas River OU 11
Soil Characteristic | Pre-Treatment | Post-Treatment
Total Metals | Elevated | Elevated
Soluble Metals | Elevated | Reduced
Soil pH | Acidic | Neutral/alkaline
Soil Fertility | Low | High
Soil Organic Matter | Low | High
Biological Function | Low | High
Erosion | High | Low

## Slide 30
10 year old treated tailings
Livestock grazing remediated land
Notes: The revegetation results of the 1998-1999 demonstration areas show the robust potential of in-situ treatment of contaminated soil and tailings without topsoil. The willows in the background were untreated and were avoided during soil treatment. This same type of approach will be used during the remedial action: preservation of existing woody vegetation wherever possible coupled with careful soil treatment with amendments for fluvial deposits.

## Slide 31: Questions/Discussion
Contact Information:
Stuart Jennings
sjennings@reclamationresearch.net