## Slide 1: NEPA & Mining 101
May 12, 2016
Cindi Godsey, Permit Writer and Alaska Mining Coordinator, US EPA Region 10
Patty McGrath, Permitting Manager, Donlin Gold LLC
Lorraine Edmond, Hydrogeologist, US EPA Region 10

## Slide 2: Mining Information Session
Module 1: Mining Fundamentals
Module 2: Environmental Concerns & Issues
(May 24th at 1 – 3 pm EDT)
Module 3: Regulatory Process & How Tribes can Engage
(June 8th at 1 – 3 pm EDT)

## Slide 3: Module 1
Mining in the U.S.
Mining Development Process
Mining Fundamentals
  Exploration
  Types of mining
  Types of mineral processing
  Mining waste products

## Slide 4: Mining Overview: Gold
US ranked 4th globally in gold production (2014)

## Slide 5: U.S. Mining Overview: Gold
Large gold mines found in NV, CO, AK, UT, SD, CA
New mine under construction in SC
New copper/gold mine potential in AK, ID, MT, MN, WI
Copper and gold mines = >70% of large U.S. facilities

## Slide 6: Mining Overview: Copper
US ranked 6th globally in copper production (2014)

## Slide 7: U.S. Mining Overview: Copper
Top copper producing states include AZ, NM, UT, NV, MT
New copper/gold mine potential in AK, ID, MT, MN, WI
Used mainly in construction (43%) and electric equipment (19%)
Copper and gold mines = >70% of U.S. mines

## Slide 8: Commodity Prices
Commodity prices have a direct effect on exploration expenditures

## Slide 9: Mining Overview: Silver
US ranked 9th globally in silver production (2014)

## Slide 10: U.S. Mining Overview: Silver
Silver produced from mines in AK, AZ, UT, NV and others
The majority of silver mining in the US is a byproduct of copper, zinc/lead and gold mining
Current uses of silver include industry electronics and energy (e.g., cell phones or solar panels)

## Slide 11: Uranium Deposits

## Slide 12: US Uranium Production
US ranked 9th globally in uranium production (2014)
U.S. uranium mines produced 3.3 million pounds of U3O8 in 2015 (DOE EIA)
  Production came from one uranium mill in Utah, and in-situ leach operations in Wyoming, Texas and Nebraska.
  This production accounts for 9% of the uranium consumed by US nuclear power plants. The remainder is imported.
US uranium reserve estimates are strongly sensitive to price.

## Slide 13: Other U.S. Metals Mining
Lead mining: MO and AK
Zinc mining: TN and AK
Phosphate mining: FL and ID
Iron ore mining: MN and MI
Molybdenum mining: AZ, CO, ID

## Slide 14: Active Metals Mines
Notes: Mine information from National Minerals Information Center of the USGS.

## Slide 15: Coal Deposits

## Slide 16: Major Steps in Mine Development
Prospecting: geological data and map reviews, non- invasive exploration
Staking: establish mining rights
Exploration (includes drilling, geophysics, bulk sampling)

## Slide 17: Cont. Major Steps in Mine Development
Assessment of mineral potential and economic feasibility
Mine development planning, environmental review and permitting process
Mine development (construction)

## Slide 18: Cont. Major Steps in Mine Development
Mine operations
Shutdown and reclamation
Long-term monitoring and site maintenance

## Slide 19: Typical Timeframe for a Successful Mine Project
Initial Exploration
Advanced Exploration
Environmental Studies
Pre-feasibility
Studies
Feasibility
Studies
NEPA & Permitting
Financing
Construction
1
2
3
4
5
6
7
8
9
10
11
12
YEARS

## Slide 20: Mineral Prospecting & Exploration

## Slide 21: Mining

## Slide 22: Lands Open/Closed to Mining
Open lands: all federal lands not specifically withdrawn from entry under the Mining Law, including national forests
Closed lands:
  Bureau of Reclamation lands
  Conservation Areas
  National Monuments and National Parks, National Wildlife Refuges
  Wild & Scenic Rivers within quarter-mile of bank
States laws are generally similar to federal laws

## Slide 23: State & Federal Mining Claims
Laws and regulations:
  1872 Mining Law + State-specific laws
Federal mining claims require a “discovery” of a “valuable deposit”
Claims are “self-initiated” and staked
  a claim is the right to explore for and extract minerals from a tract of land
Locatable minerals are claimed
  Platinum, gold, silver, copper lead, zinc, uranium…
Leasable minerals are leased through bidding
  Petroleum, coal, phosphate, sodium, potassium…

## Slide 24: State & Federal Mining Claims
Claims are held through rental fees and assessment work:
  Claims on federal land: file notice with BLM; $135/year per claim (20-160 acres)
  Claims on state land: state laws vary
Royalties during production:
  Federal: none required
  State: laws vary from none up to 10% of net income/year from mining

## Slide 25: Patents
Convert federal land to private land
There is currently a moratorium on new patenting, but patented claims are common in older mining districts, often as “in-holdings” surrounded by federal land

## Slide 26: Exploration Activities
Geologic mapping
Rock, sediment and soil geochemical sampling
Claim staking
Geophysical surveys (air & ground)
Trenching
Core or rotary drilling
Bulk sampling
Resource estimation
Early
Stage
Mid-Stage
Advanced Stage

## Slide 27: Exploration is activity spent searching for mineral deposits
Activities generally have little ground disturbance
More expensive with continued success
Permits required for ground-disturbing activities such as road building, trenching

## Slide 28: Types of Permits for Exploration
Federal Permits
  Clean Water Act 404 general permit or
  Individual for wetlands disturbance
  On federal land: approval by USFS and/or BLM
State Permits
  Vary by state
  Typically a land use permit
  Temporary water use permit

## Slide 29: Sediment Sampling

## Slide 30: Airborne Geophysics

## Slide 31: Soil Sampling to Explore for Gold
31

## Slide 32: Core Drilling

## Slide 33: What Is a Mine?
Location where rocks containing valuable minerals (ore) are extracted from the ground
Rates: 100s – 100,000s of tons/day
Types of mining:
  open pit
  underground
  strip mining
  placer mining (gold)

## Slide 34: Open Pit Mining
Ore accessed from the surface
Blasting
Haul to crusher/mill
Starting clockwise from top right, images from agnormark, sashagrunge, supapornss used with permission of Adobe Stock in this publication and future work product generated by Skeo for EPA.

## Slide 35: Open Pit Mine
Fort Knox Mine, AK

## Slide 36: Underground Mining
Ore accessed by adit, shaft and tunnel

## Slide 37: Underground Mine
Greens Creek Mine, AK

## Slide 38: Strip Mining
Topsoil Replaced/
Revegetation
Regrade
Backfilling
Active Pit
Coal
Seams
Over and Inter
Burden
Regraded Area
Topsoil
Pre-stripping/
Topsoil removal
Direction of
Mining
Spoils
Two Bull Ridge
Usibelli Coal Mine
Healy Alaska
Reclamation
Active Mining
Pre-Mining
Usibelli Coal, AK

## Slide 39: Strip Mining
Southeast Idaho Phosphate Mines

## Slide 40: Gold Placer Mining
Alaska Mechanical Dredge
Oregon Suction Dredge

## Slide 41: Mineral Processing

## Slide 42: What Is Mineral Processing?
Production of valuable metal from mined ore

## Slide 43: Mineral Processing
Valuable mineral(s) separated from waste minerals

## Slide 44: Mineral Processing Steps
Particle size reduction
  Crushing & grinding
Concentrating the valuable metal
  Gravity separation
  Flotation
  Leaching
  Others
Purifying the valuable metal
  Smelting
  Refining
  Others
Ore containing 2% cooper as chalcopyrite (copper-iron-sulfide mineral)
Flotation concentrate containing 30% copper as chalcopyrite
Smelting & refining to produce pure (99.9%) copper

## Slide 45: Crushing & Grinding
Reduce particle size to expose the target minerals.
Water is added during the grinding stage
Image from Onur Hazar Altindag used with permission of Adobe Stock in this publication and future work product generated by Skeo for EPA.
Video from Nimito used with permission of Adobe Stock in this publication and future work product generated by Skeo for EPA.

## Slide 46: Flotation
Commonly used for many minerals
Chemicals added to ground ore cause mineral particles to stick to air bubbles, create a froth, and “depress” waste minerals
  Examples: organic compounds (xanthates), cyanide, copper sulfate, zinc sulfate, oils, alcohols, lime, acids

## Slide 47: Flotation
Cross Section of a Flotation Cell

## Slide 48: Leaching
Can be used on ore or flotation concentrates
Chemical added to dissolve the valuable metal
Examples:
  cyanide is used to dissolve gold and silver from ores
  acid is used to dissolve copper and uranium from ores

## Slide 49: Vat & Tank Leaching
Image from Vividrange used with permission of Adobe Stock in this publication and future work product generated by Skeo for EPA.

## Slide 50: Heap Leaching

## Slide 51: Separation of Metal from Leach Solution
Carbon Adsorption: gold adsorbs onto carbon
Electrowinning: uses steel wool or copper as a cathode to extract the metal in acid or base solution
Precipitation: solution
combined with
chemicals to
form metal precipitate

## Slide 52: Purification and Production of Metal
Smelting and Refining
Starting clockwise from top left, images from Oleksiy Mark, nasimi, icarmen13 used with permission of Adobe Stock in this publication and future work product generated by Skeo for EPA.

## Slide 53: Example of Gold Processing

## Slide 54: Example of Gold Processing

## Slide 55: Mineral Processing
55
Red Dog Mine, AK
Bingham Canyon Mine, UT

## Slide 56: Questions and Comments
Next Webinars on NEPA and Mining 101:
May 24th
Part 2- Mining Environmental Concerns and Issues
June 8th
Part 3- The Regulatory Process and How Tribes can Engage

## Slide 57
ADOBE STOCK IMAGE / VIDEO NOTICE
This presentation contains Adobe Stock images and video that may not be used elsewhere without permission from Adobe Stock. Readers may not access or download Adobe Stock images or video from this document for any purpose and must comply with Adobe Stock’s Terms of Use, which require users to obtain a license to the work.